Robot Arm’s Serial Port Commands
# Introduction
The robot arm can communicate with the host computer through the standard host computer connector USB port. Communication uses serial port, which must be set at 115200bps, 8N1. The serial command sent by the host computer has a fixed length of 48 bytes, and the connector has a buffer of 9600 bytes. If the computer sends instructions too fast, buffer will be full and no new instructions will be received. Instructions are executed on a FIFO basis. There are replies for each received instructions, but periodically send 11 bytes of status information to host.
There are two categories of instructions:
1. Movement instructions: starting with 0xEE and ended by 0xEF
2. Control instructions: starting with 0xFC and ended by 0xFD
# List of Instructions
## Linear Interpolation Positioning Commands (Corresponding to G1)